## Slide 1
Wind Power:
An Attractive Source of Energy for Iowa and the US
Eugene S. Takle
Professor, Atmospheric Science
& Agricultural Meteorology
Director, Climate Science
Program
Iowa State University
EPSCoR Wind Webinar
Iowa State Unversity
1 April 2013

## Slide 2: Outline
Why should we care?
Emerging importance of wind power
US wind energy resources
Iowa wind energy resources
Wind energy measurements and research

## Slide 3: Wind Power
Wind is a clean (i.e., carbon-free, pollution-free) source of renewable energy
The US Department of Energy has a scenario of producing 20% of our energy supply from wind by 2030.
This will require 300 GW by 2030 (US installed capacity as of Sept 2012 was 60 GW)
Wind power, P ~  V3

## Slide 5
Projected contribution from Iowa: > 20 GW

## Slide 8
Musial, W., and B. Ram, 2010: Large-scale Offshore Wind Power in the United States. Assessment of Opportunities and Barriers. NREL/TP-500-40745. 240 pp. [Available online at http://www.osti.gov/bridge]

## Slide 10
Musial, W., and B. Ram, 2010: Large-scale Offshore Wind Power in the United States. Assessment of Opportunities and Barriers. NREL/TP-500-40745. 240 pp. [Available online at http://www.osti.gov/bridge]

## Slide 11
Musial, W., and B. Ram, 2010: Large-scale Offshore Wind Power in the United States. Assessment of Opportunities and Barriers. NREL/TP-500-40745. 240 pp. [Available online at http://www.osti.gov/bridge]

## Slide 12
Musial, W., and B. Ram, 2010: Large-scale Offshore Wind Power in the United States. Assessment of Opportunities and Barriers. NREL/TP-500-40745. 240 pp. [Available online at http://www.osti.gov/bridge]

## Slide 13
Musial, W., and B. Ram, 2010: Large-scale Offshore Wind Power in the United States. Assessment of Opportunities and Barriers. NREL/TP-500-40745. 240 pp. [Available online at http://www.osti.gov/bridge]

## Slide 16
Source: UniFly A/S
Horns Rev 1 owned by Vattenfall. Photographer Christian Steiness.

## Slide 17: Iowa’s Contribution
Iowa ranks third behind Texas and California among all states in wind generation with 5.137 GW of operating capacity (2,893 wind turbines) and gnerates 20% of total electrical energy from wind

## Slide 23
Number of Occurrences
Winspeed (m/s)
2
10
8
6
4
12
14
16
18
20
22

## Slide 24: Observed wind speed profiles (Windcube lidar, summer, Midwest US) exhibit more variability than is traditionally considered in CFD
And these are “typical” midwestern conditions!
Turbine Wake
LLJ Max
~ 12 m/s
LLJ Max
~ 16 m/s
Rhodes, Aitken, Lundquist, 2010, 2011
Julie.Lundquist@colorado.edu

## Slide 25
“Given that a 1% error in wind speed estimates for a 100 MW wind generation facility can lead to losses approaching $12,000,000 over the lifetime of that plant, a better understanding of the physical and dynamic processes across the range of scales that create a particular wind climate is needed.”
Draft recommendations, DOE Workshop on Research Needs for Wind Resource Characterization, 14-16 Jan 2008, Broomfield, CO
Iowa will have 5,317 MW installed by 2012, so a 1% error is $212 million over its lifetime.
Need Better Estimates of Wind Speed
for Forecasting Wind Power

## Slide 26: What Turbine Density Optimizes Wind Power Production and Agricultural Production?

## Slide 27: Preliminary Observations

## Slide 28: Turbine-Crop Interactions: Overview
Do turbines create a measureable influence on the microclimate over crops?
If so, does this influence create measureable biophysical changes?
And if this is so, does this influence affect yield?
Agricultural shelterbelts have a positive effect on crop growth and yield.
Will wind turbines also have a positive effect?
Photo courtesy of Lisa H Brasche

## Slide 29: Turbines offline: August 27, 2010 2300-0000 LST
Return to reference flow
conditions during the shut
down
80-m wind direction
vector
Station north of two turbine lines has 2-3X ambient TKE and Heat flux before/after OFF period

## Slide 30: Conceptual Model of Turbine-crop Interaction via Mean Wind and Turbulence Fields
__ ___________________________________
Speed recovery
CO2
H2O
Heat
day
night

## Slide 31
Photo courtesy of Lisa H Brasche

## Slide 35
Vertically Pointing Lidar
Vertical profiles of turbulence kinetic energy (TKE)
16-17 July 2010
4.5 D South of B-turbines
2.0 D North of B-turbines
TKE difference
Rotor Layer
CU/NREL/ISU Lidar deployment team

## Slide 36: Turbine Influence on Surface Fluxes
2010 NLAE Instruments (6.45 m)
Daytime fluxes
  Sensible heat: <2%
  Latent heat: <2%
  CO2 : -15% (higher uptake)
Nighttime fluxes
  Sensible heat: -2 to -4% (warms crop)
  Latent heat: +10-20% (less dew)
  CO2: +10% (more respiration)
Net ecosystem exchange*
  +18-20% (increased uptake by crop)
2011 NCAR Instruments (4.50 m)
Daytime fluxes
  Sensible heat: +5% (cools crop)
  Latent heat: +3 to +4% (dries crop)
  CO2: -5 to -10% (higher uptake)
Nighttime fluxes
  Sensible heat: -5-15% (warms crop)
  Latent heat: -20-30% (more dew)
  CO2: +5 to -5% (indeterminate)
Net ecosystem exchange*
  +10% (increased uptake by crop)
* Soil respiration not included
Same maize field
Different maize fields
Notes: Same as what was shared at Nov 29 EPSCoR meeting

## Slide 37
Measuring Wind Speed, Wind Direction, Temperature, and Turbulence with a Tethered Balloon

## Slide 40
CWEX11
REU student short course in field measurements
NCAR station records 40 m/s (89 mph)wind on 11 July
REU students measure noise levels in the wind farm

## Slide 41: Summary
The US has a very large wind energy resource potential
Iowa also has strong energy resources
Current research is seeking answers to
  How wind farms interact with crops
  How to get more energy out of existing wind farms
Wind energy has a good future in Iowa and provides a promising career for new graduates

## Slide 42
ACKNOWLEDGMENTS
Julie Lundquist for slides from presentation at LANL
Dr. Ron Huhn, property owner
Gene and Todd Flynn, farm operators
Lisa Brasche for photos
Equipment and personnel supplied by the National Laboratory for Agriculture and
the Environment
Funding supplied by
Center for Global and Regional Environmental Research, University of Iowa
MidAmerican Energy Company
Ames Laboratory , Department of Energy
National Science Foundation
Photo courtesy of Lisa H Brasche

## Slide 43: For More Information
Eugene S. Takle
gstakle@iastate.edu
http://www.meteor.iastate.edu/faculty/takle/
515-294-9871
Photo courtesy of Lisa H Brasche